## Slide 1
An Assessment Of Per-and Polyfluoroalkyl Substances (PFAS) In Food Packaging Manufactured And Retailed In Trinidad And Tobago
Shelinie Albert
University of the West Indies St. Augustine Campus, St. Augustine, Trinidad and Tobago
INTRODUCTION
Per- and polyfluoroalkyl substances (PFAS) are a diverse group of synthetic compounds widely used for their dual hydrophobic and lipophobic properties.
They are inherently persistent, and many are mobile, bioaccumulative, and toxic to both humans and environment
One of the main sources of exposure to these contaminants is via consumption particularly from food contact materials (FCM)
.
There is limited data and research undertaken in the Caribbean that addresses PFAS in food packaging
It is of particular interest as there have not been any regulatory standards adopted in Trinidad and Tobago yet that prohibits the use of single-use products containing these “forever chemicals”.
Chemical analysis techniques for the monitoring and identification of PFAS are essential to support studies of their environmental fate and transport, as well as to promote environmental regulation and remediation.
INTEGRATION OF GREEN CHEMISTRY
By identifying and isolating selective PFAS, aids in the prevention of pollution by reducing the production and use at its source and promoting safer alternatives in food packaging.
Furthermore, it reduces the production of potential harmful by-products that may form as they do not disintegrate in the environment and can exist for extensive periods of time .
FOOD
INDUSTRY
PFAS FROM FOOD PACKAGING
CROPS
HUMANS
LANDFILLS,
ENVIRONMENT
IMPORTANCE OF THIS RESEARCH
METHOD
REFERENCES
Homogenize
Extract with methanol
Sonicate and Centrifuge
Filter
Pre-concentrate
Analyse using F-19 NMR and GC-MS /MS
Haether Schwartz-Narbonne, C. X., Anna Shalin, Heather D. Whitehead, Diwen Yang, Graham F. Peaslee, Zhanyun Wang, Yan Wu, Hui Peng, Arlene Blum, Marta Venier, Miriam L. Diamond. Per-and Polyfluoroalkyl Substances in Canadian Fast Food Packaging. Environmental Science and Technology Letters 2023, 10, 343-349.
Shenglan Jia, M. M. D. S., Caixia Li, Shane A.Snyder. Recent advances in mass spectrometry analytical techniques for per-and polyfluoroalkyl substances (PFAS). Analytical and Bioanalytical Chemistry 2022, 414, 13. DOI: https://doi.org/10.1007/s00216-022-03905-y.