## Slide 1
Organic wastes treatment and bioenergy recovery from biomass through anaerobic digestion
Fatemeh Sadat Arghavan1, Louise Meunier1, Ehssan Koupaie1*
1 Department of Chemical Engineering, Smith Engineering, Queen’s University, Canada.
Relation to green chemistry
Reduction in greenhouse gas emissions Capturing and combusting methane
Diverting organic wastes from landfilling and incineration
Carbon sequestration Applying nutrient rich digestate to the land
Reduction in fossil fuel consumption Generation of renewable heat, electricity and fuel
References
Fig 4. Schematic of process for setting up co-digestion reactor. Raw sludge collected from a wastewater treatment plant was centrifuged and then thermally pretreated at 170°C for 3 hours using hydrothermal autoclave reactors. Food waste, prepared in the laboratory, was homogenized using a food processor. The two prepared feedstocks were then combined in different mixing ratios.
Digestate
Soil amendment
Liquid fertilizer
Pre-processing
Food waste
Agricultural residues
Animal manure
Sewage sludge
Hydrolysis {1}
Acidogenesis {2}
Methanogenesis {4}
Acetogenesis {3}
Electricity
Vehicle fuel
Biogas
Fig 2. Organic wastes conversion to valuable bioproducts through anaerobic digestion process. Organic wastes, either alone or combined with other feedstocks, undergo preprocessing to enhance bioavailability before entering the AD system. Microorganisms degrade and convert these materials into biogas. The remaining digestate is another valuable bioproduct of the process, widely used in the agriculture sector.
Preprocessing techniques on feedstocks
Breaking down complex compounds and making them easily accessible to microorganisms.
Advantages of applying pretreatment on feedstocks before anaerobic digestion [5]:
Increasing the soluble organic fractions: Making them more digestible by microorganisms
Reducing particles size: Increasing surface area and improving biodegradability
Increasing digestate dewaterability: Reducing post-treatment costs
Reducing pathogen: Improving digestate hygienic quality
Organic waste or feedstocks sources
Fig 3. Disruption of sludge floc structure during pretreatment techniques. Sludge flocs consist of microbial cell aggregates encapsulated by extracellular polymeric substances (EPS), which provide structural stability and protection. Pretreatment techniques disrupt this stable structure, breaking down the EPS and releasing intracellular compounds into the surrounding matrix, thereby enhancing the bioavailability of organic materials [5].
[1] Capareda, S., Introduction to biomass energy conversions. 2023: CRC press.
[2] U.S. Energy Information Administration. (n.d.). Biomass explained. Retrieved January 1, 2025, from https://www.eia.gov/energyexplained/biomass/
[3] Wei, L., et al., Anaerobic Digestion Process and Biogas Production, in Biogas Plants. 2024. p. 1-35.
[4] Vasiliadou, I.A., K. Gioulounta, and K. Stamatelatou, Chapter 9 - Production of biogas via anaerobic digestion, in Handbook of Biofuels Production (Third Edition), R. Luque, et al., Editors. 2023, Woodhead Publishing. p. 253-311.
[5] Mitraka, G.-C., et al., A Comprehensive Review on Pretreatment Methods for Enhanced Biogas Production from Sewage Sludge. Energies, 2022. 15(18): p. 6536.
Biomass as a renewable source of energy
Organic material either burned directly to generate energy or converted to liquid and gaseous fuels.
Different ways of converting biomass to bioenergy [1]:
Direct combustion to heat generation
Thermochemical conversion to produce solid, gaseous, and liquid fuels
Chemical conversion to produce liquid fuels
Biological conversion to produce liquid and gaseous fuels
Combination of two or more techniques
Fig 1. Biomass sources for energy production. Plants capture sunlight and convert it into chemical energy stored as carbohydrates through photosynthesis. Various types of biomass, rich in organic compounds, serve as renewable energy sources where the stored energy can be efficiently recovered for sustainable applications [2].
Green chemistry
Designing products and processes in a way to reduce waste, save energy, and minimize hazardous substances
Key results
Increasing methane yield by incorporating higher proportions of FW into the feedstock mixture.
Achieving the lowest COD removal efficiency (42%) with 100% TH, while 100% FW shows the highest removal efficiency (86 %).
Future directions
Using biochar as a sustainable additive to enhance anaerobic digestion performance.
Applying photocatalytic process as a low-energy alternative to sludge thermal pretreatment.
Chart: Mixing ratio (TH:FW)
| 100-0 | 80-20 | 60-40 | 40-60 | 20-80 | 0-100
 | 38.213 | 50.2615 | 57.6237 | 68.8348 | 76.2029 | 86
Chart: Time (Day)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 19 | 20 | 21 | 24 | 27 | 30 | 34 | 37
100 TH | 0 | 3.5418 | 9.055 | 14.1421 | 21.4429 | 27.641 | 33.3463 | 39.4108 | 46.2856 | 53.8035 | 63.0172 | 74.4111 | 86.089 | 98.8611 | 113.8803 | 127.5547 | 136.9354 | 143.0333 | 151.7124 | 155.864 | 158.4201 | 160.759 | 164.4261 | 166.1302 | 168.87 | 169.2793
80 TH:20 FW | 0 | 10.3136 | 18.4011 | 24.8378 | 32.2916 | 38.8199 | 45.1565 | 52.2518 | 60.0642 | 69.2773 | 80.1995 | 94.0316 | 108.0305 | 122.6297 | 138.5045 | 152.2032 | 162.6753 | 170.6127 | 178.0665 | 182.1102 | 184.8033 | 187.2212 | 190.7897 | 192.1237 | 194.3832 | 194.6583
60 TH:40 FW | 0 | 17.9425 | 27.7813 | 34.1853 | 41.8273 | 49.3585 | 56.8319 | 64.8202 | 73.0747 | 83.0112 | 94.5675 | 108.7511 | 121.5696 | 133.6318 | 150.9219 | 165.2164 | 177.9754 | 190.2995 | 204.4298 | 212.5779 | 218.2717 | 223.686 | 227.791 | 230.4405 | 233.1121 | 233.9065
40 TH:60 FW | 0 | 25.1262 | 38.1549 | 46.5652 | 54.3957 | 62.2548 | 69.7337 | 78.0489 | 87.8181 | 99.5354 | 113.6665 | 130.2589 | 144.7226 | 156.9531 | 170.5045 | 186.3272 | 202.8245 | 218.0675 | 233.5385 | 241.5877 | 247.7932 | 257.7904 | 263.3783 | 267.0084 | 270.3725 | 271.0948
20 TH:80 FW | 0 | 33.1135 | 48.0165 | 56.7225 | 63.4517 | 70.0288 | 77.1761 | 84.5325 | 93.4572 | 105.2522 | 121.4763 | 142.6808 | 163.2769 | 180.4799 | 197.2743 | 215.2282 | 231.3002 | 245.9466 | 263.3682 | 271.9507 | 278.6799 | 292.3853 | 300.3975 | 304.8266 | 308.3623 | 309.0941
100 FW | 0 | 47.0375 | 64.4265 | 73.6904 | 80.169 | 85.0266 | 90.0176 | 97.3579 | 106.8219 | 118.4607 | 134.8187 | 158.2144 | 183.0822 | 204.5799 | 223.0102 | 239.5939 | 253.5256 | 271.2173 | 294.0436 | 304.6924 | 312.3508 | 328.0573 | 340.7887 | 345.7438 | 349.5704 | 350.2578
Conclusion
Enhancing methane yield and COD removal efficiency by mixing sludge with food waste in anaerobic digestion process.
Fig 5. COD removal efficiency and cumulative methane yield for various mixing ratios of TH and FW.
6 + radiant energy
Photosynthesis equation
Cell wall
Cell membrane
Cytoplasm
Pretreatment
Pretreatment
Sewage sludge
Rupture of sludge flocs
Cell lysis
Wood
Crops
Oils and fats
Garbage
Sewage
Animal manure
Anaerobic digestion
Biochemical process that converts organic material into valuable products under no oxygen conditions [3].
Lab-scale project
Anaerobic co-digestion (AnCoD) of food waste (FW) and thermal pretreated sludge (TH).
Objectives:
Investigation of the effect of mixing ratios of FW and TH on AnCoD performance
Investigation of the performance of AnCoD in removing chemical oxygen demand (COD)
Investigation of the effect of thermal hydrolysis on sludge degradability
Four phases of anaerobic digestion [4]:
Hydrolysis: Conversion of complex biopolymers to simple monomers
Acidogenesis: Conversion of simple molecules generated in hydrolysis to volatile fatty acids
Acetogenesis: Conversion of volatile fatty acids to acetate, hydrogen, and carbon dioxide
Methanogenesis: Conversion of acetate, carbon dioxide, and hydrogen to methane gas